## Slide 1: Mutual Attestation of IoT Devices TCG Members Meeting June 2015 Edinburgh
Prof. Andreas Steffen
Institute for Internet Technologies and Applications
HSR University of Applied Sciences Rapperswil
andreas.steffen@hsr.ch

## Slide 2: Where the heck is Rapperswil?
HSR

## Slide 3: HSR - Hochschule für Technik Rapperswil
University of Applied Sciences with about 1500 students
Faculty of Information Technology (300-400 students)
Bachelor Course (3 years), Master Course (+1.5 years)

## Slide 4: strongSwan – the OpenSource VPN Solution
Corporate Network
Linux FreeRadius Server
Windows Active Directory Server
Internet
High-Availability strongSwan VPN Gateway
Windows 7/8 Agile VPN Client
strongSwan Linux Client
Notes: N Rekeying Notification (optional)
SAi Suite of cryptographic proposals for the Child SA (ESP and/or AH)
Ni Initiator Nonce
KEi Initiatior public factor for the Diffie-Hellman Key Exchange (optional PFS)
TSi Initiator Traffic Selectors (subnets behind the Initiator)
TSr Responder Traffic Selectors (subnets behind the Responder
SA1r Selection of a cryptographic proposal for the IKE SA
Nr Responder Nonce
KEr Responder public factor for the Diffie-Hellman Key Exchange (optional PFS)
TSi Initiator Traffic Selectors (subnets behind the Initiator)
TSr Responder Traffic Selectors (subnets behind the Responder

## Slide 5: Mutual Attestation of IoT Devices TCG Members Meeting June 2015 Edinburgh
Trusted Network Communications (TNC)
Current Use Cases:
Network Access Control & Endpoint Compliance

## Slide 6: TNC Architecture
RFC 5792
RFC 5793
RFC 6876 RFC 7171
VPN Client
VPN Gateway
Lying Endpoint
Endpoint
Compliance
Network Access Control
Notes: Abbreviations
• AR Access Requestor • IF Interface • IMC Integrity Measurement Collector • IMV Integrity Measurement Verifier • M Measurement • PDP Policy Decision Point • PEP Policy Enforcement Point • T Transport • TNC Trusted Network Connect

## Slide 7: Network Endpoint Assessment (RFC 5209)
NEA Server
NEA Client
Posture
Broker
Client
Posture
Collectors
(1 .. N)
Posture
Collectors
(1 .. N)
Posture
Collectors
(1 .. N)
Posture
Broker
Server
Posture
Collectors
(1 .. N)
Posture
Collectors
(1 .. N)
Posture
Validators
(1 .. N)
Posture
Transport
Clients
(1 .. K)
Posture
Transport
Clients
(1 .. K)
Posture
Transport
Clients
(1 .. K)
Posture
Transport
Clients
(1 .. K)
Posture
Transport
Clients
(1 .. K)
Posture
Transport
Servers
(1 .. K)
PA
PB
PT
RFC 5792 PA-TNC
RFC 5793 PB-TNC
RFC 6876 PT-TLS RFC 7171 PT-EAP
Notes: Abbreviations
• PA Posture Attribute Protocol • PB Posture Broker Protocol • PT Posture Transport Protocol
PA Subtypes
• 0 Testing • 1 Operating System (OS) • 2 Anti-Virus • 3 Anti-Spyware • 4 Ant-Malware • 5 Firewall • 6 Intrusion Detection and/or Prevention (IDPS) Software • 7 Virtual Private Network (VPN) Software • 8 NEA Client Software
PT Protocols
• e.g. EAP-TLS via 802.1X (Layer 2) or IKEv2 (Layer 3)

## Slide 8: Layered TNC Protocol Stack
[IMV] operating system name is 'Android' from vendor Google
[IMV] operating system version is '4.2.1‘
[IMV] device ID is cf5e4cbcc6e6a2db
[TNC] received TNCCS batch (160 bytes) for Connection ID 1
[TNC] PB-TNC state transition from 'Init' to 'Server Working'
[TNC] processing PB-TNC CDATA batch
[TNC] processing PB-Language-Preference message (31 bytes)
[TNC] processing PB-PA message (121 bytes)
[TNC] setting language preference to 'en‘
[NET] received packet: from 152.96.15.29[50871] to 77.56.144.51[4500] (320 bytes)
[ENC] parsed IKE_AUTH request 8 [ EAP/RES/TTLS ]
[IKE] received tunneled EAP-TTLS AVP [EAP/RES/PT]
[TNC] handling PB-PA message type 'IETF/Operating System' 0x000000/0x00000001
[IMV] IMV 1 "OS" received message for Connection ID 1 from IMC 1
[TNC] processing PA-TNC message with ID 0xec41ce1d
[TNC] processing PA-TNC attribute type 'IETF/Product Information' 0x000000/0x00000002
[TNC] processing PA-TNC attribute type 'IETF/String Version' 0x000000/0x00000004
[TNC} processing PA-TNC attribute type 'ITA-HSR/Device ID' 0x00902a/0x00000008
IF-T Transport Protocol PT-EAP (RFC 7171)
IF-M Measurement Protocol PA-TNC (RFC 5792)
IF-TNCCS TNC Client-Server Protocol PB-TNC (RFC 5793)
TNC Measurement Data

## Slide 9: PB-TNC / IF-TNCCS 2.0 State Machine
Exchange of PB-TNC Client/Server Data Batches containing PA-TNC Messages
Notes: PA-TNC IF-TNCCS 2.0 Batch Types
• CDATA ClientData • SDATA ServerData • CRETRY ClientRetry • SRETRY ServerRetry • RESULT Result • CLOSE Close

## Slide 10: Mutual Attestation of IoT Devices TCG Members Meeting June 2015 Edinburgh
Trusted Network Communications (TNC)
New Use Case:
Mutual Measurements of Endpoints

## Slide 11: Example: Mutually Trusted Video Phones
Notes: PA-TNC IF-TNCCS 2.0 Batch Types
• CDATA ClientData • SDATA ServerData • CRETRY ClientRetry • SRETRY ServerRetry • RESULT Result • CLOSE Close

## Slide 12: Mutual Attestation of IoT Devices
IoT Device 2
Video Link
IoT Device 1
Video Link
IKEv2
TNC Client
TNC Server
TPM
Attestation IMC
Attestation IMV
PT-EAP
DB
Linux IMA*
TNC Client
TNC Server
TPM
Attestation IMC
Attestation IMV
PT-EAP
DB
IPsec
DB
Trusted Reference DB
TLS
TLS
DB
DB
OS IMC
Linux IMA
Linux OS
Linux OS
OS IMC
* IMA: Integrity Measurement Architecture
Notes: PA-TNC IF-TNCCS 2.0 Batch Types
• CDATA ClientData • SDATA ServerData • CRETRY ClientRetry • SRETRY ServerRetry • RESULT Result • CLOSE Close

## Slide 13: Why do Mutual TNC Measurements work?
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Version |D| Reserved | B-Type| +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Batch Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Directionality (D) (1 bit)
When a Posture Broker Client is sending this message, the Directionality bit MUST be set to 0. When a Posture Broker Server is sending this message, the Directionality bit MUST be set to 1. This helps avoid any situation where two Posture Broker Clients or two Posture Broker Servers engage in a dialog. It also helps with debugging.
Definition of PB-TNC Batch Header in RFC 5793
Idea: Use the Directionality Flag to multiplex two IF-TNCCS 2.0 connections in opposite directions over a common IF-T transport channel.

## Slide 14: PB-TNC Mutual Capability Announcement
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Flags | PB-TNC Vendor ID | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | PB-TNC Message Type | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | PB-TNC Message Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |H|F| Reserved | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
PB-TNC Vendor ID (24 bits) 0x00902A (ITA-HSR)
PB-TNC Message Type (32 bits) 0x00000001 (PB-Mutual-Capability)
PB-TNC Message Type (32 bits) 16 (bytes)
Half-Duplex Capability (H) (1 bit) Full-Duplex Capability (F) (1 bit)
.
PB-Mutual-Capability Message defined in ITA-HSR Namespace

## Slide 15: Mutual Measurements in Half-Duplex Mode
Initiator |  | PB-TNC Batch[PB-TNC Messages] |  | Responder
TNC Client |  | CDATA[PB-MUTUAL, PB-PA] |  | TNC Server
TNC Client |  | SDATA[PB-MUTUAL, PB-PA] |  | TNC Server
TNC Server |  | SDATA[] |  | TNC Client
TNC Server |  | CDATA[PB-PA] |  | TNC Client
TNC Client |  | CDATA[PB-PA] |  | TNC Server
TNC Client |  | RESULT[PB-ASSESSMENT] |  | TNC Server
TNC Server |  | SDATA[PB-PA] |  | TNC Client
TNC Server |  | CDATA[PB-PA] |  | TNC Client
TNC Server |  | RESULT[PB-ASSESSMENT] |  | TNC Client
TNC Server |  | CLOSE[] |  | TNC Client
TNC Client |  | CLOSE[] |  | TNC Server
The initiating TNC client sends CLOSE batch last
Works over PT-EAP and PT-TLS

## Slide 16: Mutual Measurements in Full-Duplex Mode
Initiator |  | PB-TNC Batch[PB-TNC Messages] |  | Responder
TNC Client |  | CDATA[PB-MUTUAL, PB-PA] |  | TNC Server
TNC Client |  | SDATA[PB-MUTUAL, PB-PA] |  | TNC Server
TNC Server |  | CDATA[PB-PA] |  | TNC Client
TNC Client |  | CDATA[PB-PA] |  | TNC Server
TNC Server |  | SDATA[PB-PA] |  | TNC Client
TNC Client |  | RESULT[PB-ASSESSMENT] |  | TNC Server
TNC Server |  | CDATA[PB-PA] |  | TNC Client
TNC Server |  | RESULT[PB-ASSESSMENT] |  | TNC Client
TNC Server |  | CLOSE[] |  | TNC Client
TNC Client |  | CLOSE[] |  | TNC Server
The initiating TNC client sends CLOSE batch last
Works over PT-TLS only

## Slide 17: Conclusions
Mutual TNC measurements can be easily implemented without changes in the existing PB-TNC IETF standard.
The announcement of the mutual TNC measurement capability is done via a PB-Mutual-Capability PB-TNC message currently defined in the ITA-HSR namespace.
If the mutual TNC measurement capability is of general interest then the announcement message should be standardized either in the TCG or IETF namespace.
Another interesting use case for the mutual measurement capability would be an initiating endpoint wanting to attest a cloud server before connecting to it.

## Slide 18
Thank you for your attention!
Questions? www.strongswan.org/tnc/